## Slide 1
INDIA_CRYPTO_SOC
AES-CA Accelerated RISC-V SoC
for Indian Government Document Encryption
Aadhaar PDF
UIDAI / Biometric
Gov Document
NIC / DigiLocker
Medical Record
ABDM / HL7 FHIR
RV32IM Core · AES-256 4-CA · MS-TRNG · AXI Firewall · PULP Peripherals

## Slide 2
SoC Architecture — Block Diagram
2M × 8S AXI-Lite Crossbar
CPU Subsystem
RV32IM Core
5-Stage Pipeline
AES ISA Ext
Custom-0 Sideband
AXI-Lite Crossbar · 2 Masters × 8 Slaves
m0: CPU dmem | m1: PDF DMA
Memory
Boot ROM
32 KB · s0
0x0000_0000
SRAM
128 KB · s1
0x2000_0000
Port A: imem
Port B: dmem+DMA
Crypto Engines [Firewall Protected]
AES-CA Accel
4-CA AES-256 CTR · s2
0x3000_0000
MS-TRNG
Metastable FF · SP 800-90B · s3
0x3000_1000
India PDF Engine
Aadhaar · GovDoc · Medical · s4
0x3000_2000
Secure Peripherals [Firewall Protected]
Secure UART
PULP apb_uart · s5
0x4000_0000
Secure I2C
PULP apb_i2c · s6
0x4000_1000
Secure SPI
PULP apb_spi_master · s7
0x4000_2000

## Slide 3
Memory Map & Address Space
Address Range | Size | Module | Slave | Protected
0x0000_0000 – 0x0000_7FFF | 32 KB | Boot ROM | s0 | No
0x2000_0000 – 0x2001_FFFF | 128 KB | SRAM | s1 | No
0x3000_0000 – 0x3000_0FFF | 4 KB | AES-CA Accel | s2 | Firewall
0x3000_1000 – 0x3000_1FFF | 4 KB | MS-TRNG | s3 | Firewall
0x3000_2000 – 0x3000_2FFF | 4 KB | India PDF Engine | s4 | Firewall
0x4000_0000 – 0x4000_0FFF | 4 KB | Secure UART | s5 | Firewall
0x4000_1000 – 0x4000_1FFF | 4 KB | Secure I2C | s6 | Firewall
0x4000_2000 – 0x4000_2FFF | 4 KB | Secure SPI | s7 | Firewall
AXI Masters
m0: CPU dmem — trusted, HIGH priority
m1: PDF DMA — semi-trusted, LOW priority
Firewall Default Permissions
Slave | CPU(m0) | DMA(m1)
s2 AES-CA | YES | NO
s3 TRNG | YES | NO
s4 PDF | YES | NO
s5-s7 | YES | NO
DMA (m1) may access SRAM (s1) directly — no firewall. CPU writes perm_table to grant DMA access to other slaves.

## Slide 4
RV32IM Core — Microarchitecture
5-Stage Pipeline + Attack Protections
IF
Instruction
Fetch
ID
Decode +
RegFile Read
EX
ALU +
MUL/DIV
MEM
AXI-Lite
Bus Access
WB
Result
Write-Back
PC + Branch Pred
ECC RegFile Read
Parity Check
Firewall Access
ECC Write-Back
Instruction Parity
Each fetched instruction carries a parity bit. Mismatch raises an illegal-instruction trap.
PC Range Guard
CSRs 0xBC0/0xBC1 set min/max valid PC. Out-of-bounds fetch halts pipeline.
Register File ECC
Hamming(7,4) per nibble. Corrects 1-bit errors. Flags 2-bit (fatal) errors.
24-bit Watchdog
Reloads on every committed instruction. Reset if no progress detected.
Custom CSRs (RV32IM)
0xBC0 pc_min_guard min valid PC
0xBC1 pc_max_guard max valid PC
0xBC2 wdt_reload 24-bit watchdog value
M-Extension (Iterative)
MUL, MULH, MULHSU, MULHU
DIV, DIVU, REM, REMU
(Multi-cycle iterative, no DSP required)
AES Custom-0 Sideband
custom_valid + custom_instr[31:0]
custom_rs1[31:0] + custom_rs2[31:0]
→ AES ISA Ext (combinational)
→ custom_rd[31:0] back to regfile
Instructions: aes.esb aes.emx aes.esr
aes.dsb aes.dmx aes.disr aes.xk aes.rcon

## Slide 5
AES-CA Accelerator — 4-CA Microarchitecture
1
CA-1 SubBytes + Neighbour Perturbation
128-bit state through AES S-box; each byte XOR'd with CA-1 neighbours (row-wise)
2
CA-2 ShiftRows
Byte rotation: row i shifted left by i positions (0,1,2,3 byte shifts)
3
CA-3 MixColumns over GF(2⁸)
4×4 byte-matrix MDS multiplication; polynomial x²+x+1 in GF(2⁸)
4
CA-4 AddRoundKey + Rule-90 CA
256-bit key XOR; Rule-90: state[i] = state[i-1] XOR state[i+1] across 128-bit row
AES-256 · 14 rounds · CTR Mode · Encrypt = Decrypt (same hardware) · direct_key[255:0] · direct_din/dout[127:0]
CTR Mode
Same HW for Encrypt & Decrypt
E: AES(counter) XOR plaintext
= ciphertext
D: AES(counter) XOR ciphertext
= plaintext
Counter is always forward-encrypted
Direct Interface (PDF Engine)
direct_key[255:0]
direct_din[127:0]
direct_start
direct_decrypt
direct_dout[127:0]
direct_done
14 rounds total
Key schedule expanded from 256-bit to 240 bytes (60 words)

## Slide 6
Encryption & Decryption Flow
AES-256 CTR + CA-HMAC Authentication
ENCRYPT
DECRYPT
1 Collect Entropy
Poll MS-TRNG STATUS until valid=1, read DATA × 12 times
8 words → KEY regs, 4 words → NONCE regs
2 Configure PDF Engine
Set APP_MODE, SRC_ADDR, DST_ADDR, PDF_LEN
Write DOC_ID, TIMESTAMP, AUTH_LEVEL
3 Load KEY + NONCE
Write KEY[0..7] and NONCE[0..3] from TRNG reads
256-bit key + 128-bit nonce loaded
4 Start Engine
Write CTRL = 0x05 (START | IRQ_EN)
Wait for interrupt (ext_irq to CPU)
5 Engine Streams Output
Encrypted Header → Encrypted PDF bytes → CA-HMAC Tag
All images + text encrypted together
6 Read Result Tag
Read RESULT_TAG[0..3] from PDF Engine
Store 128-bit tag alongside document
1 Load Pre-shared Keys
Write KEY[0..7] and NONCE[0..3]
Same key+nonce used during encryption
2 Load Expected Tag
Write EXP_TAG[0..3] (stored from encryption)
128-bit CA-HMAC for authentication
3 Configure Addresses
SRC_ADDR = ciphertext in SRAM
DST_ADDR = output location, PDF_LEN
4 Start Engine
Write CTRL = 0x07 (START | DECRYPT | IRQ_EN)
Wait for interrupt
5 Engine Decrypts + Verifies
Recomputes CA-HMAC tag over decrypted data
Compares vs EXP_TAG
auth_ok = 1
Plaintext valid
at DST_ADDR
auth_fail = 1
HW zeroes DST_ADDR
Do NOT use output

## Slide 7
MS-TRNG & India PDF Engine
Entropy Source + Streaming Crypto Engine
MS-TRNG — Metastable True RNG
8-Channel
Metastable
FF Capture
(dual-edge)
Von Neumann
Debiaser
(pair XOR)
Galois LFSR
Masker
(whitening)
RCT + APT
Health Tests
SP 800-90B
trng_data
[31:0]
trng_valid
AXI-Lite Slave @ 0x3000_1000
0x00 STATUS [0]=valid
0x04 DATA 32-bit random word (read clears valid)
0x08 HEALTH [1]=APT_fail [0]=RCT_fail
0x0C CTRL [0]=enable [1]=rst_health
Dual-edge capture: posedge + negedge FF per channel. Metastability provides thermal noise entropy. Galois LFSR masks bias. Health tests continuously validate output quality.
India PDF Engine — 17-State FSM
Output Packet Format:
Encrypted
Header
APP_MODE·DOC_ID
TIMESTAMP
Encrypted PDF
Binary Stream
text + images + fonts
entire file
CA-HMAC
Tag
128-bit
Rule-30 ×8
Key Registers @ 0x3000_2000
0x000 CTRL [0]=START [1]=DECRYPT [2]=IRQ_EN
0x004 APP_MODE 0=Aadhaar 1=GovDoc 2=Medical
0x008 STATUS busy/done/auth_ok/auth_fail/error
0x00C SRC_ADDR Input PDF base in SRAM
0x010 DST_ADDR Output base in SRAM
0x014 PDF_LEN Byte count (multiple of 16)
0x018 NONCE[0..3] 128-bit nonce (4 words)
0x028 KEY[0..7] 256-bit AES key (8 words)
APP_MODE=0
Aadhaar
Face photo
Fingerprint
Iris scan
APP_MODE=1
GovDoc
Scanned pages
Signatures
Seals
APP_MODE=2
Medical
DICOM images
X-rays
Reports

## Slide 8
AXI-Lite Fabric & Firewall
m0: CPU dmem
HIGH priority trusted
m1: PDF DMA
LOW priority semi-trusted
AXI
Lite
Xbar
s0 Boot ROM
s1 SRAM
s2 AES-CA [FW]
s3 TRNG [FW]
s4 PDF [FW]
s5 UART [FW]
s6 I2C [FW]
s7 SPI [FW]
SRAM (s1) has no firewall — DMA accesses SRAM directly via xbar.
AXI Firewall — Per Protected Slave
32-bit perm_table [ slave*4 + master ]
Write-once lock (write 0xDEADBEEF to LOCK_TABLE)
Denied access logged to LAST_DENIED_ADDR
DENY_COUNT [15:0] incremented on each block
SLVERR returned to master on denied access
Firewall Register Map
0x00 PERM_TABLE [31:0]
0x04 LOCK_TABLE write 0xDEADBEEF
0x08 LAST_DENIED_ADDR [31:0]
0x0C LAST_DENIED_MASTER [1:0]
0x10 DENY_COUNT [15:0]
Default (after reset):
CPU (m0) -> s2..s7 : ALLOW
DMA (m1) -> s2..s7 : DENY

## Slide 9
Secure Peripherals — PULP Platform + Security Wrappers
apb_uart · apb_i2c · apb_spi_master
Secure UART
PULP apb_uart + axil_to_apb
0x4000_0000
RX Glitch Filter
3-sample stability vote on RX input
Secure-mode TX Gate
Silences TX, flushes RX on lockout
Frame-Error Detection
Counts and alerts on framing errors
Baud-Rate Lock
Write 0xA5 to LOCK reg; prevents MITM
LOCKED + ATTACK_ALERT
Status bits [5][6] in STATUS register
0x00 DATA TX write / RX read
0x04 STATUS [7:0] flags
0x08 BAUD clock divisor
0x0C CTRL TX_EN/RX_EN/FIFO_CLR
0x10 LOCK write 0xA5
Secure I2C
PULP apb_i2c + axil_to_apb
0x4000_1000
4-Entry Address Whitelist
Only whitelisted 7-bit addresses pass
Bus Stuck Detection
500k cycles timeout → asserts BUS_STUCK
9-Pulse SCL Recovery
Automatic recovery sequence on stuck bus
SDA Glitch Filter
3-stage majority voter on SDA input
Secure-mode Lockout
Blocks all I2C transactions when active
0x00 CTRL START/STOP/RW/ACK_EN
0x10 STATUS [6:0] flags
0x14 PRESCALE SCL divider
0x18 WL_CTRL whitelist ctrl
0x1C WL_ADDR 7-bit address entry
Secure SPI
PULP apb_spi_master + axil_to_apb
0x4000_2000
HW CS Guard
Firmware cannot hold CS low manually
Transfer Length Cap
MAX_LEN[7:0] limits bytes per transaction
Per-CS Permanent Lock
CS_LOCK[3:0] write-once disables CS pin
Overflow / Underrun Alert
ALERT[1:0] flags on FIFO errors
Secure-mode Lockout
Forces CS_N=1111, blocks all SPI
0x00 DATA TX write / RX read
0x08 CTRL START/CPOL/CPHA/LOOPBACK
0x0C CS_SEL one-hot chip-select
0x14 MAX_LEN max transfer bytes
0x18 CS_LOCK permanent CS disable

## Slide 10
Attack Protection Summary
CPU Core Protections
Instruction parity check → trap on mismatch
PC range guard (CSR 0xBC0/BC1) → halt on OOB
Register file ECC Hamming(7,4) → correct 1-bit, flag 2-bit
24-bit watchdog → reset on stall
AXI Firewall
Per-(master,slave) permission table [32-bit]
Write-once lock (0xDEADBEEF)
Denied access logging + deny counter
SLVERR on unauthorized access
Default: CPU-only on s2–s7
Secure UART & I2C
UART: RX glitch filter (3-sample vote)
UART: Baud-rate lock (0xA5 write-once)
UART: Frame-error attack detection
I2C: 4-entry 7-bit address whitelist
I2C: Bus-stuck (500k) + 9-pulse recovery
SPI & PDF Engine
SPI: HW CS guard — no soft CS hold
SPI: Transfer length enforcement (MAX_LEN)
SPI: Per-CS permanent lockout register
PDF: CA-HMAC on every document
PDF: Auth-fail → HW zeroes output region

## Slide 11
Target Applications
Aadhaar · Government Document · Medical Record
01
APP_MODE = 0
Aadhaar PDF
UIDAI / Biometric Data
Contains:
Face photograph (JPEG)
Fingerprint minutiae
Iris scan data
UID number + QR code
All data encrypted as
one binary blob.
Auth-level: restricted
Authority: UIDAI
02
APP_MODE = 1
Gov Document
NIC / DigiLocker / IT Act 2000
Contains:
Scanned document pages
Digital signatures
Official seals / stamps
Form data + images
DOC_ID + TIMESTAMP
in encrypted header.
Auth-level: secret
Authority: NIC / DigiLocker
03
APP_MODE = 2
Medical Record
ABDM / HL7 FHIR / DICOM
Contains:
DICOM image slices
X-ray / MRI / CT scans
Lab reports + results
Doctor prescriptions
CA-HMAC ensures
zero-tamper integrity.
Auth-level: top-secret
Authority: ABDM / NHA