## Slide 1
INDIA_CRYPTO_SOC
Secure Cryptographic SoC for PDF & Image Processing
TSMC 28nm HPC | Die: ~0.648 mm² | 250 MHz @ 0.9V
Notes: Welcome slide. INDIA_CRYPTO_SOC is a full custom secure SoC targeting TSMC 28nm HPC for PDF and image cryptographic processing.

## Slide 2
System Overview
Core Modules
RV32IM 5-stage pipeline CPU with AES ISA extensions
AES-256 CTR + Cellular Automaton (CA) accelerator
India PDF Engine — 17-state streaming FSM
Ring-Oscillator TRNG (SP 800-90B)
AXI-Lite 2-master × 8-slave crossbar
AXI Firewall — 16-entry write-once table
PULP UART, I2C, SPI (APB bridges)
Dual-port SRAM: 32 KB IMEM + 32 KB DMEM
Boot ROM: 32 KB
0.648
mm² Total Die
250
MHz @ 0.9V
285
MB/s AES Throughput
Notes: The SoC integrates a hardened RISC-V core, AES-256 with cellular automaton rounds, a streaming PDF engine, and a compliant TRNG — all in under 0.65 mm² at 28nm HPC.

## Slide 3
Top-Level Architecture
Masters
CPU dmem
(AXI Master m0)
PDF DMA
(AXI Master m1)
AXI-Lite Crossbar
2M × 8S
AXI Firewall
16-entry permission table
8 Slaves
s0 Boot ROM
s1 SRAM
s2 AES-CA
s3 TRNG
s4 PDF Engine
s5 FW CSR
s6 UART
s7 I2C/SPI
Firewall: 32-bit permission per (master,slave) pair | Lock: 0xDEADBEEF
Notes: Two AXI masters — the CPU data bus and the PDF DMA — connect through an 8-slave crossbar. Every path passes through the AXI Firewall with write-once permissions.

## Slide 4
CPU Core — RV32IM Pipeline
IF
→
ID
→
EX
→
MEM
→
WB
Security Features
Instruction parity trap at fetch stage
PC Range Guard: CSR 0xBC0/0xBC1
Register file ECC: Hamming(7,4)
24-bit Watchdog Timer (WDT)
AES ISA Extensions (Custom-0)
aes_enc_round
aes_dec_round
aes_keygen_assist
aes_subbytes
aes_shiftrows
aes_mixcols
aes_addkey
aes_ctr_inc
Combinational sideband — zero pipeline stalls
Notes: The CPU is a hardened RV32IM with three layers of fault detection: parity at fetch, ECC on registers, and PC range enforcement. The 8 custom AES instructions execute combinationally with no pipeline stall.

## Slide 5
AES-256 Cellular Automaton Accelerator
CA-1 SubBytes + Rule-90 Perturbation
CA-2 ShiftRows (Standard)
CA-3 MixColumns in GF(2⁸)
CA-4 AddRoundKey + Rule-30 Perturbation
14
AES-256 Rounds
~100K
Gate Equivalents
285 MB/s
@ 250 MHz throughput
Supports ENCRYPT and DECRYPT | 16-byte block streaming | CTR mode
Notes: AES-256 uses 14 rounds, each of which passes through four custom Cellular Automaton transformations that add nonlinear perturbation on top of the standard AES operations.

## Slide 6
India PDF Engine — Streaming Crypto FSM
IDLE
HEADER
KEY_LOAD
IV_GEN
CTR_INIT
STREAM_IN
AES_PROC
CA_HMAC
STREAM_OUT
VERIFY
DONE
→ flow
APP_MODE 0
PDF Encryption
SPI → AES-CTR → SPI
APP_MODE 1
PDF Decryption
Reverse path
APP_MODE 2
HMAC Verify
Tag-only check
CA-HMAC: Rule-30 based | 8 iterations | 256-bit output
Processes entire PDF binary — text + embedded images — as byte stream
Notes: The PDF engine is a 17-state FSM that handles the full lifecycle of a document — parse header, load key from I2C, generate IV from TRNG, then stream the entire binary through AES-CTR in 16-byte blocks.

## Slide 7
TRNG Architecture — 28nm HPC Upgrade
Original Design
8-channel Metastable FF
(Dual-edge sampling)
Von Neumann Debiaser
Galois LFSR
SP 800-90B: RCT + APT
Issue: metastability window narrows at 28nm — entropy loss per channel
28nm HPC Upgrade
Synthesized Ring-Oscillator
Jitter Source
Von Neumann Debiaser [retained]
Galois LFSR [retained]
SP 800-90B: RCT + APT [retained]
23 Mb/s @ 23 pJ/b demonstrated in 28nm CMOS (ISSCC 2023)
Pin 10 (rosc_ext): external clock injection for ring-osc frequency dithering
Notes: At 28nm, transistor metastability windows shrink, reducing raw entropy per metastable FF channel. ISSCC 2023 demonstrated a synthesized ring-oscillator TRNG achieving 23 Mb/s at 23 pJ/b in 28nm — we adopt this approach.

## Slide 8
AXI Firewall — Hardware Security Perimeter
Permission Table (16 entries)
Master
Slave
Perm Word [31:0]
CPU
SRAM
0xFFFFFFFF (full)
CPU
PDF Eng
0x0000FFFF (read-only)
DMA
SRAM
0xFFFF0000 (write-only)
DMA
CPU CSRs
0x00000000 (denied)
Write-Once Lock
Write 0xDEADBEEF → table read-only forever
Deny Logging
Unauthorized access logged + IRQ raised
Address Truncation
32-bit FW output [11:0] → 12-bit slave ports
Notes: The AXI Firewall enforces isolation between the CPU data bus and the DMA data path. A write-once lock mechanism prevents run-time permission escalation — once set, the table is hardware immutable.

## Slide 9
Memory Architecture — 28nm HPC Sizing
Memory | Size | Port | Words × Width | Function
IMEM | 32 KB | Port A | 8192 × 32b | Instructions + boot firmware
DMEM | 32 KB | Port B | 8192 × 32b | Data + stack + AES buffer
Boot ROM | 32 KB | Single | 8192 × 32b | NOP sled + reset vectors
Total | 96 KB | — | — | On-chip memory
Key Insight: PDF Engine uses AES-CTR block streaming — DMEM holds only 16-byte working blocks, not the full PDF. 32 KB DMEM is sufficient.
RTL: localparam SRAM_WORDS = 16384
Notes: We reduced SRAM from 128 KB to 64 KB by exploiting the streaming nature of AES-CTR. At 28nm, 64 KB SRAM fits in 0.110 mm² — enabling the design to close timing and area.

## Slide 10
28nm HPC Area — Literature-Grounded Estimates
Trikarenos Silicon (TVLSI 2024)
Process: TSMC 28HPC+
3x Ibex RISC-V cores (lockstep)
256 KB ECC SRAM = 0.55 mm²
Logic = 0.15 mm²
Total die = 2.0 mm²
250 MHz @ 0.9V, 15.7 mW
→ Effective: 1.55 μm²/GE, 0.269 μm²/bit
Component | Area | Status
Logic 220K GE | 0.341 mm² | —
SRAM 64 KB | 0.110 mm² | —
Boot ROM 32KB | 0.017 mm² | —
Pad ring 10p | 0.150 mm² | —
Core total | 0.468 mm² | ✓ target ≤ 0.5
Total die | 0.648 mm² | ✓ target ≤ 1.0
TSMC 28nm HP 6T SRAM cell = 0.127 μm²/bit (reference)
Notes: All area estimates are calibrated against the Trikarenos chip — real taped-out silicon on TSMC 28HPC+. Our logic gate count is higher due to AES-CA, but we achieve smaller SRAM by streaming.

## Slide 11
10-Pin I/O Assignment
Pin # | Name | Direction | Function
— | clk | IN | System clock (given, not counted)
1 | rst_n | IN | Active-low async reset
2 | spi_mosi | IN | PDF data in from host
3 | spi_miso | OUT | Encrypted PDF to host
4 | spi_sck | IN | SPI clock
5 | spi_cs_n | IN | SPI chip select
6 | uart_rx | IN | Command channel
7 | uart_tx | OUT | Response + IRQ mux (idle-muxed)
8 | i2c_sda | BIDIR | Key provisioning / OTP
9 | i2c_scl | IN | I2C clock
10 | rosc_ext | IN | Ring-osc dither / TRNG seed
[SPI] PDF data plane [UART] Control plane [I2C] Key management plane
Notes: All 10 signal pins are accounted for. SPI handles bulk PDF streaming. UART handles control commands. I2C is the secure key provisioning channel — isolated from the SPI data plane at the firewall level.

## Slide 12
End-to-End PDF Encryption Flow
1
Host sends PDF
via SPI (spi_mosi)
→
2
PDF DMA
(AXI master m1)
writes DMEM
→
3
CPU triggers
PDF Engine
APP_MODE=0
→
4
FSM: HEADER_PARSE
→ KEY_LOAD (I2C OTP)
→ IV_GEN (TRNG)
↓
5
AES-CA: 14 rounds
16-byte blocks
285 MB/s
←
6
CA-HMAC appended
Rule-30 × 8 iter
256-bit tag
←
7
Encrypted output
streams via SPI
(spi_miso) to host
Notes: The encryption flow is fully pipelined: while AES-CA processes block N, the DMA is already streaming block N+1. The CA-HMAC tag is appended at the end before the final SPI burst.

## Slide 13
End-to-End PDF Decryption Flow
APP_MODE = 1 | AES-256 CTR Inverse | CA-HMAC Verification Before Plaintext Release
1
Host sends
Encrypted PDF
via SPI (spi_mosi)
Ciphertext + HMAC tag
2
PDF DMA
writes DMEM
AXI master m1
32 KB working buffer
3
CPU triggers
PDF Engine
APP_MODE = 1
via AXI-Lite
4
FSM:
Header + IV Extract
IV read from
ciphertext header
5
AES-CA
Decryption
14 rounds inverse
InvSubBytes+InvMixCols
6
CA-HMAC
Verification
Rule-30 x 8 iter
Tag match check
7
Plaintext out
via SPI
spi_miso to host
Only if HMAC valid
Key Differences vs Encryption
IV Source: Extracted from ciphertext header — NOT generated by TRNG
AES-CA Mode: Inverse rounds — InvSubBytes + InvShiftRows + InvMixColumns + InvAddRoundKey
CA-HMAC: Verified first — plaintext ONLY released if tag matches (APP_MODE 1 safety gate)
Failure action: HMAC mismatch → IRQ raised, SPI output blocked, deny_log written — no partial plaintext

## Slide 14
SoC Die Floorplan & PCB Reference Layout
Left: Die Floorplan (TSMC 28nm HPC, 0.648 mm²) | Right: Reference PCB Layout (40mm × 30mm)

## Slide 15
Die Floorplan — Block Area Breakdown
TSMC 28nm HPC · Core: ~0.468 mm² · Total Die: ~0.648 mm² · 250 MHz @ 0.9V
Block | Area | Notes
SRAM 64 KB | 0.110 mm² | 32 KB IMEM (Port A) + 32 KB DMEM (Port B)
Boot ROM 32 KB | 0.017 mm² | NOP sled (0x00000013) + reset vectors
AXI Crossbar | 0.031 mm² | 2-master × 8-slave AXI-Lite fabric
AXI Firewall | 0.019 mm² | 16-entry write-once permission table
RV32IM CPU Core | 0.070 mm² | 5-stage pipeline + ECC + WDT + AES ISA ext
AES-CA Accel | 0.155 mm² | AES-256 CTR + 4 CA rounds (~100K GE)
India PDF Engine | 0.023 mm² | 17-state streaming FSM + CA-HMAC
Ring-Osc TRNG | 0.005 mm² | SP 800-90B compliant, 23 Mb/s @ 23 pJ/b
APB Bridges x3 | 0.023 mm² | UART + I2C + SPI peripheral bridges
Core Total | 0.468 mm² | Target <= 0.5 mm2 CHECK

## Slide 16
Security Architecture — Four Pillars
CPU Hardening
Parity trap at fetch | PC Range Guard CSR 0xBC0/0xBC1
Hamming(7,4) ECC registers | 24-bit Watchdog
Crypto Strength
AES-256 CTR + CA perturbation (Rule-90/30)
CA-HMAC: Rule-30 × 8 iter, 256-bit
TRNG SP 800-90B (RCT+APT)
Access Control
AXI Firewall 16-entry table | Write-once lock 0xDEADBEEF
Deny logging + IRQ | DMA / CPU stack isolation
Key Security
Keys via I2C only | Never on SPI data plane
CA-HMAC binds ciphertext to key
Firewall enforces key isolation
Notes: Security is layered across four domains: CPU hardening prevents software exploits, crypto strength resists cryptanalysis, access control isolates hardware domains, and key security prevents exfiltration.

## Slide 17
Summary
Full RV32IM + AES-256 CA SoC in 0.648 mm² at TSMC 28nm HPC
Streaming PDF crypto — AES-CTR block mode, no full-file SRAM required
10-pin constrained design — SPI + UART + I2C fully plane-separated
Area calibrated from Trikarenos silicon (TVLSI 2024) + ISSCC 2023 TRNG data
Hardware AXI Firewall isolates CPU, DMA, and key management planes
Architecture ready for Aadhaar biometric secure element integration
INDIA_CRYPTO_SOC | 28nm HPC | aasheiksaran1033@gmail.com
Notes: INDIA_CRYPTO_SOC achieves a complete cryptographic SoC in under 0.65 mm² by combining streaming AES-CTR architecture, a hardened RISC-V core, and hardware-enforced isolation — all calibrated against published 28nm silicon.